## Slide 1
01
Sampling, analysis and interpretation of atmospheric aerosol particles
Summer school lecture
Online instruments, offline samples, and source interpretation

## Slide 2
02
Air as the first exposure
Aerosol measurements matter because people breathe continuously
Without | Typical survival time
Food | Weeks
Water | Days
Air | Minutes
Air quality begins with the particles people inhale.

## Slide 3
03
Aerosol particles in the atmosphere
Small abundance can still have large atmospheric effects
- Particles scatter and absorb radiation
- Particles act as cloud condensation nuclei
- Particle surfaces carry chemistry and biological exposure
- Size and composition control the effect
The same mass can mean very different particle numbers.

## Slide 4
04
The measurement chain
Sampling decisions shape every result that follows
Step | Question
Sampling | What reaches the instrument or filter?
Analysis | Which property do we measure?
Quality checks | Can we trust the number?
Interpretation | What source or process explains it?
Bad sampling cannot be repaired by good statistics.

## Slide 5
05
Online and offline measurements
Real-time dynamics and laboratory detail answer different questions
Approach | Strength | Typical limitation
Online | Minutes to seconds | Usually fewer chemical targets
Offline | Detailed chemistry | Time-integrated sample

## Slide 6
06
SMPS
A real-time view of particle number size distributions
The output is concentration by mobility diameter and time.

## Slide 7
07
Inside an SMPS
Charge, classify, count
Neutralizer
DMA
CPC

## Slide 8
08
DMA choice
The selected classifier sets the useful size window
Classifier | Use
Nano DMA | Small particles and nucleation mode
Long DMA | Wider or larger submicron range

## Slide 9
09
Reading SMPS contours
Growth appears as a rising size band over time
- Time on the x-axis
- Particle diameter on the y-axis
- Color shows number concentration

## Slide 10
10
Aethalometer
Optical absorption gives near-real-time carbonaceous aerosol information
Signal | Interpretation
880 nm absorption | Common equivalent black carbon channel
370 to 950 nm range | Wavelength dependence of absorption
AAE | Clue for source and brown-carbon influence
AE31 and AE33 instruments use seven wavelengths.

## Slide 11
11
Black and brown carbon
Seven wavelengths help separate soot-like and organic light absorption
Material | Typical optical behavior
Black carbon | Strong absorption across visible wavelengths
Brown carbon | Stronger absorption toward UV and blue light
Separation | Model-based estimate using wavelength dependence
Do not call the split purely mechanical. It depends on assumptions.

## Slide 12
12
Aerosol mass spectrometry
Online chemistry joins size information with composition
What AMS adds | Why it matters
Non-refractory chemistry | Sulfate, nitrate, ammonium, organics
Fast time resolution | Events and changing sources
Mass spectra | Chemical fingerprints

## Slide 13
13
Offline sampling
Filters turn air into a preserved analytical sample
- Known flow rate
- Known sampling time
- Known inlet cut point
- Filter selected for later analysis

## Slide 14
14
Gravimetric analysis
Mass concentration comes from a controlled weighing difference
Quantity | Meaning
Pre-weight | Clean conditioned filter
Post-weight | Loaded conditioned filter
Air volume | Flow multiplied by time
PM mass concentration | Mass difference divided by air volume
Temperature and humidity control are part of the measurement.

## Slide 15
15
Size-resolved offline sampling
Cascade impactors separate particles by aerodynamic diameter
- Large particles impact first
- Smaller particles reach later stages
- Each stage can be analyzed chemically

## Slide 16
16
Denuders and sampling artefacts
The sampler can change the sample
Artefact | What happens
Positive | Gas adsorbs on the filter
Negative | Collected material evaporates
Denuder | Removes selected gases before collection

## Slide 17
17
Storage and blanks
A filter remains chemically active after sampling
- Use field blanks and laboratory blanks
- Avoid contamination during transport
- Control light, temperature, and humidity
- Freeze or cool samples when the target compounds require it
- Document the chain of custody
The archive is useful only when the history is known.

## Slide 18
18
Extraction strategy
The solvent follows the compound class
Target | Common strategy
Ions and WSOC | Water extraction
WIOC and organics | Organic solvent extraction
Metals | Acid digestion or direct elemental analysis
Volatile organics | SPME or thermal desorption

## Slide 19
19
Carbon fractions
OC, EC, WSOC, and WIOC depend on operational definitions
Fraction | How to explain it
OC | Carbon that evolves in the organic-carbon part of the method
EC | Refractory light-absorbing carbon by thermal-optical split
WSOC | Organic carbon extracted into water
WIOC | Organic carbon remaining outside the water-soluble fraction
Protocol choice can affect the OC and EC split.

## Slide 20
20
GC-MS and thermal desorption
Volatile and semi-volatile compounds need gentle transfer
Trap, desorb, separate, detect.

## Slide 21
21
LC-MS
Polar and soluble organics often require liquid chromatography
- Extract into a compatible solvent
- Clean or concentrate with SPE when needed
- Separate by LC before mass spectrometry
- Quantify target compounds by calibration

## Slide 22
22
HRMS and triple quadrupole MS
Discovery and quantification use different strengths
Instrument | Best teaching role
HRMS | Molecular formula clues and non-target screening
Triple quadrupole | Sensitive targeted quantification

## Slide 23
23
Elements and metals
Inorganic tracers connect particles to sources and processes
Tracer group | Possible interpretation
Crustal elements | Dust and resuspension
Sea salt ions | Marine influence
V, Ni | Oil combustion or shipping influence
K | Biomass burning influence
Pb, Zn, Cu | Industry, traffic, or brake and tire wear
Tracers suggest sources. They rarely prove a source alone.

## Slide 24
24
Interpretation goals
The same data can serve monitoring, mechanism, or source analysis
Goal | What the data must support
Monitoring | Comparable measurements over time
Science | New compounds and mechanisms
Episodes | Timing and meteorology
Source apportionment | Patterns that separate source influence
Choose the method after choosing the question.

## Slide 25
25
PCA
Principal components summarize covariance patterns
PCA output | How to read it
Loadings | Which variables move together
Scores | When each pattern is strong
Components | Mathematical patterns, not sources by themselves
PCA is a starting point for interpretation.

## Slide 26
26
Source apportionment workflow
Interpretation combines chemistry, time, and air-mass context
Input | Role
Chemical species | Source fingerprints
Size fractions | Formation and removal processes
Time patterns | Emissions and photochemistry
Meteorology | Transport and dilution
Model output | Hypotheses to test
The best interpretation explains more than one line of evidence.

## Slide 27
27
Take-home messages
Good aerosol interpretation starts before the sample exists
- Online instruments reveal fast atmospheric dynamics
- Offline samples provide richer laboratory chemistry
- Sampling artefacts can change carbon and semi-volatile results
- Extraction and instrument choice must follow the target compounds
- Source interpretation needs chemistry plus atmospheric context

## Slide 28
28
Questions
Sampling, analysis, interpretation
From air to data to explanation