## Slide 1
FROM SENSORS TO ENVIRONMENTAL INTELLIGENCE

## Slide 2
Talk Overview
Six stops from raw sensor data to environmental intelligence
01
MOTIVATION
The environmental data challenge: why collection alone is not enough
02
ARCHITECTURE
The end-to-end data lifecycle, from sensing to intelligence
03
DATA QUALITY
Automated QA/QC, calibration and environmental compensation
04
DATA FUSION
Harmonisation and the raw-to-intelligence data architecture
05
AI & ANALYTICS
From trusted data to prediction, forecasting and decision support
06
IN PRACTICE
Platform integration and applications: AirSensis & FROSTDEFEND
A single reusable platform underlies every application above.
From Sensors to Environmental Intelligence
2

## Slide 3
The Environmental Data Challenge
Why collection alone is not enough
Heterogeneous inputs
Multiple manufacturers Different pollutants & units Different sampling rates External weather and reference data
Data quality risks
Missing data & communication gaps Noise, spikes & flat-lines Drift and cross-sensitivity Temperature / humidity effects
Operational requirements
Near-real-time processing Historical analytics Traceability & provenance Integration with external systems
The goal: convert distributed raw measurements into consistent, trustworthy and reusable environmental information.
From Sensors to Environmental Intelligence
3

## Slide 4
The End-to-End Environmental Data Lifecycle
A single pipeline from observation to decision
Data provenance and traceability are maintained across every transformation.
SENSE
1
2
3
CONNECT
VALIDATE
8
Environmental
observations
Streaming &
batch ingestion
4
QA/QC &
quality flags
5
PROCESS
Calibration &
harmonisation
6
STORE
Time-series &
metadata
7
ANALYSE
AI &
analytics
INTEGRATE
APIs &
services
9
ACT
Alerts &
decisions
IoT & Edge
COLLECT
From Sensors to Environmental Intelligence
4

## Slide 5
Data Gathering: Multi-Source by Design
Sensor-agnostic acquisition for environmental monitoring
ENVIRONMENTAL OBSERVATION LAYER
Air Quality
PM₁ • PM₂.₅ • PM₁₀ NO₂ • O₃ • CO • SO₂ VOC/TVOC • CO₂
Meteorology
Temperature • RH • Pressure Wind • Rainfall • Solar
Reference & Lab
Reference instruments Co-location datasets Laboratory calibration
External Sources
Weather APIs Earth observation Existing monitoring networks
From Sensors to Environmental Intelligence
5

## Slide 6
IoT Connectivity & Edge Acquisition
Reliable field-to-cloud data transfer
FIELD
Sensors Stations Gateways
CONNECTIVITY
Wi-Fi Ethernet 4G / 5G NB-IoT LoRaWAN
PROTOCOLS
MQTT HTTP(S) REST API
CLOUD INGESTION
Authentication Buffering Validation Routing
EDGE
Time Local buffer Store & forward Retries
Resilience principle: temporary connectivity loss should not automatically become permanent data loss.
From Sensors to Environmental Intelligence
6

## Slide 7
Scalable Data Ingestion
A common entry point for heterogeneous environmental data
Real-time streams
Continuous sensor and station observations
Batch ingestion
Historical files, laboratory datasets, backfills
External APIs
Meteorology, public datasets, third-party services
INGESTION LAYER
Authentication Schema validation Normalization Routing Monitoring
COMMON OBSERVATION MODEL
Device
Sensor / Parameter Value + Unit Timestamp Location Quality / Metadata
From Sensors to Environmental Intelligence
7

## Slide 8
From Raw Measurements to Trusted Data
Separate data maturity levels instead of overwriting observations
L0
RAW
Original observations
L1
VALIDATED
Structural checks + QA/QC
L2
CORRECTED
Cleaning + calibration
L3
HARMONISED
Units + timestamps + formats
L4
DERIVED
Aggregates + indicators
L5
INTELLIGENCE
Forecasts + alerts + decisions
Reprocessing is reproducible because the original measurement and processing history are preserved.
From Sensors to Environmental Intelligence
8

## Slide 9
Automated Data Quality Assurance
Quality control is a platform service, not a manual afterthought
Flag questionable data — do not silently destroy provenance.
Range / physical limits
Missing values
Spikes & outliers
Flat-line detection
Rate-of-change
Duplicate data
Timestamp consistency
Communication gaps
Cross-sensor consistency
Sensor drift
Environmental interference
Sensor health
QUALITY FLAGS
VALID
SUSPECT
INVALID
MISSING
CALIBRATED
ESTIMATED
From Sensors to Environmental Intelligence
9

## Slide 10
Calibration & Environmental Compensation
Transform sensor response into a traceable corrected measurement
INPUTS
• Raw sensor response y
• Temperature T
• Relative humidity RH
• Context / co-pollutants x
CALIBRATION MODEL
ŷ = f(yraw, T, RH, x)
OUTPUT
• Corrected value ŷ
• Uncertainty / confidence
• Calibration version
• Quality information
Supported approaches: laboratory calibration • field co-location • multivariate models • ML • drift correction
From Sensors to Environmental Intelligence
10

## Slide 11
Harmonisation, Processing & Data Fusion
Move from device-specific measurements to a common environmental information model
Temporal processing
Resampling Synchronisation Interpolation Rolling statistics
Harmonisation
Unit conversion Naming conventions Common timestamps Metadata mapping
Sensor processing
Calibration Drift correction Outlier handling Missing-data handling
Data fusion
Multi-sensor consensus Reference integration Spatial combination Uncertainty
DERIVED PRODUCTS
AQ indicators
Exceedances
Exposure metrics
Statistics
Spatial layers
From Sensors to Environmental Intelligence
11

## Slide 12
Environmental Data Architecture
Raw, trusted and derived information coexist
INTELLIGENCE
AI • forecasts • risk • alerts
DERIVED
AQI • statistics • exposure
CALIBRATED
Corrected values • uncertainty
VALIDATED
QA/QC • quality flags
RAW
Original immutable observations
CONTEXT & PROVENANCE
• Device & sensor metadata
• Location & deployment
• Configuration history
• Calibration models & versions
• Quality flags
• Processing lineage
• User / tenant ownership
Architecture principle: never lose the path from the original observation to the final information product.
From Sensors to Environmental Intelligence
12

## Slide 13
AI & Advanced Environmental Analytics
Trusted data becomes the foundation for prediction and decision support
Sensor Intelligence -
Hardware Level
• Automated calibration
• Drift detection
• Sensor-health monitoring
• Anomaly detection
Data Intelligence -
Data Level
• Missing-data imputation
• Denoising
• Data fusion
• Uncertainty estimation
Environmental Intelligence -
Domain Level
• Air-quality forecasting
• Pollution-event detection
• Spatial estimation
• Exposure / risk analysis
MEASURE
VALIDATE
UNDERSTAND
PREDICT
ACT
From Sensors to Environmental Intelligence
13

## Slide 14
Platform Integration: Data In, Intelligence Out
The platform can be the user-facing solution or the environmental data backbone
ENVIRONMENTAL
DATA PLATFORM
Ingestion
QA / QC
Processing
Storage
AI / Analytics
Sensors
Field air-quality sensors
Stations
Reference monitoring stations
Weather
Meteorology & external feeds
External APIs
Third-party & public datasets
Dashboards
Customer Apps
GIS / BI
Research
Authorities
From Sensors to Environmental Intelligence
14

## Slide 15
One Core Platform, Multiple Environmental Applications
Reuse the same data and intelligence services across domains
ENVIRONMENTAL INTELLIGENCE PLATFORM
Dashboards & Applications
Alerts & Decision Support
AI & Analytics
Data Processing / QA/QC
Data Management & Storage
IoT / API Integration
Device & Sensor Management
AirSensis
Air-quality monitoring analytics & visualisation
FROSTDEFEND
Microclimate forecasting & warning
The strategic asset is the reusable platform underneath the applications.
From Sensors to Environmental Intelligence
15

## Slide 16
The Environmental Data Value Chain
Increasing value at every stage
The platform transforms measurements into decisions while preserving traceability across the complete lifecycle.
1
RAW DATA
What happened?
Sensor measurements
Raw Data
2
TRUSTED DATA
Can we trust it?
QA/QC • calibration
Trusted Data
3
INFORMATION
What does it mean?
Indicators • context
Information
4
KNOWLEDGE
Why is it happening?
Patterns • analytics
Knowledge
5
PREDICTION
What happens next?
Forecasts • risk
Prediction
6
ACTION
What should we do?
Alerts • decisions
Action
From Sensors to Environmental Intelligence
16

## Slide 17
From Monitoring to Environmental Intelligence
The evolution of an environmental platform
TRADITIONAL MONITORING
Sensors
Database
Dashboard
ENVIRONMENTAL INTELLIGENCE
Sensors
Trusted Data
Integrated Platform
AI / Prediction
Decision Support
Action
We do not simply collect environmental data.
We build the infrastructure that turns sensor observations into trusted, interoperable and actionable environmental intelligence.
From Sensors to Environmental Intelligence
17

## Slide 18
THANK YOU — QUESTIONS & DISCUSSION